## Slide 1: Observational Astronomy
July 30, 2026
<number>
Direct imaging
Photometry
Kitchin pp. 187-217, 276-309
Notes: <number>

## Slide 2: Astronomical Imaging
<number>
or
Specific goal:
As many objects as possible (e.g. clusters, star-forming regions)
As large range of surface brightness as possible (e.g. galaxies)
Wide
Deep
Notes: <number>

## Slide 3: Wide Field Imager: VST
<number>
The VST is a 2.6m f/5.5 Cassegrain telescope
Corrected FoV is 1.5º square with angular resolution of 0.5”
Focal plane is equipped with a 16kx16k CCD mosaic camera with a 15 pixel
Notes: <number>

## Slide 4: VST Optics
<number>
Optical layout including ADC, field corrector etc.
Plate scale:
  focal length=2.6m5.5=14.3m
  1”=  /180º/3600≈510-6 rad (1 rad ≈ 200000”)
  Resolution element: 0.5”  0.5  510-6 rad  14.3m ≈ 35 ≈ 2.3 CCD pixel (nearly perfect Nyquist sampling)
Notes: <number>

## Slide 5: Sampling Theorem (Whittaker-Nyquist-Kotelnikov-Shannon sampling theorem)
<number>
The sampling frequency must be greater than twice the bandwidth of the input signal in order to “perfectly” reconstruct the original
For Gaussian PSF with  =HWHM and 2/ - maximum frequency. Thus FWHM=
Different samplings: -Once per period
-Twice per period
-Nyquist sampling
Notes: <number>

## Slide 6: Non-dedicated telescope
<number>
VLT+FORS
FOcal Reducer/low dispersion Spectrograph
VLT UT (8.2m f/13.4): focal length=8.2m13.4=108.8m Plate scale in Cassegrain: 510-6 rad  108.8m ≈ 530/arcsec
Notes: <number>

## Slide 7: Focal Reducers
<number>
Purpose: adjusting plate scale
Side benefits: collimated beam is good for filters
Notes: <number>

## Slide 8: NOT workhorse: ALFOSC
<number>
Notes: <number>

## Slide 9: Unconventional instrument: FORS
<number>
Two resolutions: 0.2” and 0.1” by changing collimators and CCD binning
Notes: <number>

## Slide 10: Filters
<number>
Broad band filters (UBV system, Johnson H.L. & Morgan W.W.: 1953, ApJ, 117, 313)
Notes: <number>

## Slide 11: Broad-Band Filter Technology
<number>
Color absorption glasses:
blocking (high absorption shorter than certain wavelength while highly transparent at longer wavelengths) or
bell-curve (sharp cut-off at shorter wavelength and gradual drop towards longer wavelength)
Transmission is high, up to 75-90%
Notes: <number>

## Slide 12: Narrow-Band Filter Technology
<number>
Interference coatings:
Multiple (up to 20) dielectric layers producing interference between internal reflections
Create multiple transparency windows at different wavelengths
Must be combined with broad-band filters
Transmission is low, around 20-30%
Notes: <number>

## Slide 13: Chromatism and other problems
<number>
Filters are best used in parallel beam, otherwise they introduce chromatism
They also shift focal plane (transparent glass plates)
Slight tilt is used to avoid ghosts (shift of optical axis) and fringing
Transmitted light
Reflected light
Notes: <number>

## Slide 14: Transmission Function
<number>
Notes: <number>

## Slide 15: Photometry
<number>
Classical one-channel photometer:
Notes: <number>

## Slide 16: What do we measure and how?
<number>
Magnitudes:
Filters:
a and b are selected such that Vega will be 0 magnitude in all colors
Interstellar extinction: objects with the same SED located in different directions and distances will have different magnitudes (The main source of extinction is the scattering and absorption-heating of the dust particles and their main effect is to "redden" the energy distribution). Color excess:
Notes: <number>

## Slide 17: More What and How (II)
<number>
The variation of extinction with wavelength is similar for all directions: we measure color excess in one band then scale it to other bands.
Knowing scaling parameters (in principle) allows to convert apparent magnitudes m to absolute magnitudes M. Absolute magnitude is the apparent magnitude of the same object at a distance of 10 parsecs: d is the distance and A is the interstellar extinction, which can be estimated from the color excess in B-V and scaled:
Notes: <number>

## Slide 18: More What and How (III)
<number>
Absolute magnitude M does not a measure the total irradiance.
Bolometric magnitude M(bol) is defined as the absolute magnitude that would be measured by an ideal bolometer exposed to all of the radiation from an object in space.
The relation between bolometric magnitude and the absolute magnitude MV requires the knowledge of the bolometric correction B.C.:
Traditionally B.C. for solar-type stars is set close to 0 and it grows for hotter and cooler objects.
Notes: <number>

## Slide 19: Absolute and differential photometry
<number>
Radiation in a given band is affected by the atmosphere, telescope, photometer and detector. All of these must be calibrated.
Absolute photometry is done either from space or with absolute calibration e.g. against a black body standard source.
Notes: <number>

## Slide 20: Absolute and differential photometry (cont’d)
<number>
Once absolute measurements are done for a few objects they can be used as standards.
Differential photometry measures flux difference in a given band between a target and a standard.
Observations should be close on the sky and in time.
Classical sequence: <selecting band>:<standard> - <target> - <standard>
Notes: <number>

## Slide 21: CCD Photometry
<number>
Many objects at once (standards and targets)
Large dynamic range
PSF is spread over several pixels
Pixels have different sensitivity and color sensitivity
Photometry of extended sources
Notes: <number>

## Slide 22: Next time…
<number>
Astronomical detectors
Notes: <number>