## Slide 1: Observational Astronomy
PhD course by Nikolai Piskunov piskunov@astro.uu.se phone: 018 471 58 59

## Slide 2: Requirements to pass:
Attend lectures
Do home work, turn it in or report in class
Do labs
Take an exam: oral or written
Book: Kitchin: Astrophysical Techniques, IoP, 4th edition

## Slide 3: Why do we need telescopes?
Track objects on the sky
Collect photons and create image of a region on the sky (FOV)
Achieve high angular resolution
Feed multiple instruments

## Slide 4: Why telescopes can help? (Tracking objects)
Zelentchuk 6m BTA, Russia
© Istituto e Museo di Storia della Scienza
Telescope mounts:
Equatorial
  German mount
  Fork mount
  English mount
Alt-Azimuth

## Slide 5: Telescope focii
Primary
Cassegrain
Nasmyth
Coudé
?
DAO
LBT

## Slide 6: Telescope mounts: equatorial versus alt-azimuth
Gravity center location and flexure in alt-azimuth mount the support force passes precisely through the gravity center thus canceling any torque: very important for large and heavy telescopes
Field of view behavior while tracking In any focus located on the tube of an equatorially mounted telescope the field of view does not rotate
ESO 3.6m La Silla
ESO VST

## Slide 7: Home work:
Look at the BWT and answer the following questions:
  While tracking does one need to change the azimuthal velocity?
  If yes, when the azimuthal velocity is largest?
  How does the field of view rotate?
Look at the optical scheme of coudé train of an equatorially mounted telescope at figure how the field of view rotates

## Slide 8: Tracking: offset guiding
Telescope FOV
Offset guide pickup mirror
Possible locations of the pickup mirror
Telescope focal plane

## Slide 9: Collecting photons
Keck I & II | 2 x 10.0m | Mauna Kea, Hawaii | Segmented telescopes, interferometer.
Hobby-Eberly | 9.2m | Mt Fowlkes, Texas | A fixed elevation, low cost spectroscopic telescope.
Subaru | 8.3m | Mauna Kea, Hawaii | Active telescope made in Japan.
VLT | 4 x 8.2m | Cerro Paranal, Chile | ESO flagship.
Gemini | 2 x 8.0m | Mauna Kea, Hawaii Cerro Pachon, Chile | Twin 8-m telescopes in the Northern and Southern hemispheres.
Magellan | 2 x 6.5m | Las Campanas, Chile | Twin 6.5-m telescopes; also known as the Walter Baade and Landon Clay telescopes.
MMT | 6.5m | Mt Hopkins, US, Az | Replacement of the 4.2-m Multi-Mirror Telescope
BTA | 6.0m | Nizhny Arkhyz, Russia | Breaking limits, and the first large alt-azimuth telescope

## Slide 10: Optomechanics
Tracking must be very smooth
Excitation sources: mechanical noise and wind
Higher vibration frequencies have lower amplitude
Important design target: make resonance frequencies of the telescope as high as possible (>10 Hz)

## Slide 11: Angular resolution
Angular resolution goes as wavelength/diameter or baseline
Interferometers
ESO OWL 100m design

## Slide 12: Little bit of history
Galileo Galilei (1564-1642)
Telescope description published in Sidereus Nuncius (Starry Messenger) 1610
With permission of the Master and Fellows of Trinity College Cambridge

## Slide 13: Refractors
Refractors are based on lenses Easy to make, can combine several elements
Chromatic aberrations:
Largest refractor (1897): Yerkes Obs. 40”, f/19
1.2 m

## Slide 14: Reflectors
Lots of options: from basic single mirror to Newtonian and Cassegrain

## Slide 15: Summary: refractors
Axial symmetry
Combination of multiple elements
Compact
Cheap for small sizes
Chromatism
Difficult making many meter size lenses
Heavy
Impossible to make segmented lenses

## Slide 16: Summary: reflectors
Light (high surface/weight ratio)
Can be made in large sizes from temperature insensitive materials
Can be made in large sizes
Can be made segmented
Shape can be adjusted (“flexible” mirrors)
Difficult to combine
Hard to make axial systems (vigneting)

## Slide 17: Specialized telescopes:
Wide field (Schmidt camera)
Infra-red (coatings, thermal control)
Automatic/robotic telescopes (complex telescope control system)
Solar telescopes (heat)
With fixed primary (Large&Cheap)
Home work: find one example of each specialized telescope in the list above and prepare a short description of what is different, why and how it is done?

## Slide 18: Conclusions:
Binoculars, photo and video cameras, small telescopes – refractors
Intermediate size telescopes – combined reflectors/refractors
Large telescopes - reflectors

## Slide 19: Next time…
Telescope optical designs
Aberrations
Active optics
Adaptive optics
Optical components and coatings