## Slide 1: Observational Astronomy
TELESCOPES
Kitchin pp.44-88

## Slide 2: Optical Schemes
Spherical mirrors cannot focus light properly due to spherical aberrations:

## Slide 3: Optical Schemes
… but a single parabola can produce perfect image on the optical axis: Off-axis images suffer from coma.

## Slide 4: Ritchey-Chrétien telescope
Parabolic primary and hyperbolic secondary solve main aberration problems (spherical and coma) in a rather large field of view (few arcminutes) in Cassegrain focus

## Slide 5: RC design: compromises & tools
Average image quality (aberrations)
Curvature of the focal plane (trade with FoV)
Field of view of up to 2º
VISTA 4m IR survey telescope

## Slide 6: Schmidt-Cassegrain
RC provides very good image quality in a relatively small field
When large FoV (up to 5º) is need Schmidt-Cassegrain is the preferred design:
Spherical mirror
Correction plate

## Slide 7: Alternatively Gregorian system
Concave secondary after the primary focus:
Courtesy of MPI Potsdam

## Slide 8: Materials
Low thermal expansion: zerodur & sitall
mean linear coefficient of thermal expansion within temperature range -60º to +60º С is <10-8 cm ºC-1
Astro-sitall blank at LZOS (VST, VISTA, SALT, LAMOST, OWL?)
Zerodur VLT primary at REOSC

## Slide 9: More materials
Silicon Carbide
Low thermal expansion (not as good as glass)
Very light
Very hard, keep the shape well
Hard to make in large pieces
Fragile, hard to process
SiC 60 cm X-ray mirror Weight: 6.2 kg

## Slide 10: Mirror manufacturing

## Slide 11: Coatings
Mirrors:
  Aluminum with SiO on the top
  Silver-based coatings. Needs coating to prevent mechanical damage during washing
Lenses: MgF2

## Slide 12
Hard Gold coating results (from 0.7 µm to 25 µm)
Wavelength (µm)
EXAMPLES OF OPTICAL COATING
Enhanced Silver coating results (from 350 nm to 800 nm)
Wavelength (nm)
Reflectivity
Reflectivity

## Slide 13: Point Spread Function
PSF is the intensity distribution in the focal plane produced by a point source.
Ideal PSF (Bessel function)

## Slide 14: Active optics
Large thin mirrors are shaped by support system: VLT mirror is 8.2m in diameter and only 18 cm thick!
Compensate for thermal and orientation distortions
Close loop operation during adjustment
Low frequency: 30 s cycle
VLT: 150 actuators

## Slide 15: Home work
Look at the IDL program I used to illustrate spherical and parabolic mirrors. Try to compute ray-tracing for non-axial beam for a parabola.
Extend the calculations to an RC system for the brave …
- curvature
- conic constant: <-1 hyperbola, -1 parabola

## Slide 16: Next time…
… Space Telescopes (Oleg Kochukhov)