## Slide 1: Observational Astronomy
July 30, 2026
<number>
SPECTROSCOPY and spectrometers
Kitchin, pp. 310-370
Notes: <number>

## Slide 2: Spectroscopic methods
<number>
Different purposes require different instruments
Main spectroscopic methods:
  Spectrophotometry
  Low resolution
  Long slit, high resolution
  High resolution
Spectroscopic observations are characterized by: dispersion/spectral resolution and spectral range
Notes: <number>

## Slide 3: Spectrophotometry
<number>
Typical goal: search for objects with specific spectral features
Method 1: objective prism, telescope "sees" the source through a prism, therefore each point source looks like a small spectrum
Method 2: narrow band filters for given spectral features. Often such filters have the possibility to change central wavelength by changing temperature/pressure. There is no slit!
Notes: <number>

## Slide 4: Gratings
<number>
Interference:
Grating formula:
W

Blaze angle
Conventional grating
Echelle grating
ptical
ath
ifference
Notes: <number>

## Slide 5: A bit of math:
<number>
Expression for angular dispersion is found by differentiating the grating eq.:
Linear dispersion is readily obtained for a given focal length
Angular dispersion
Linear dispersion
Notes: <number>

## Slide 6: … and some more …
<number>
Angular resolution. Think of a grating as a mirror, its diffraction angle is given by:
… and combining it with the angular dispersion equation:
Resolving power depends in the number of illuminated grooves!
?
Projected size of the grating
Notes: <number>

## Slide 7: Free spectral range
<number>
The free spectral range (FSR) of a diffraction grating is defined as the spectral interval in a given order which does not overlap with the wavelengths in adjacent orders.
Order m-1
Order m
Order m+1
For a prism FSR is the whole sp. range!
Notes: <number>

## Slide 8: Grating spectrometers
<number>
Grating
Camera
Detector
Collimator
Slit
Notes: <number>

## Slide 9: Real world: the seeing and the pixel size
<number>
The angular slit size as seen by the grating is: where is the focal length of the collimator and s is the linear width of the slit. Grating equation connects this to the angular resolution element:
If we try to match this to the angular resolution of the grating we end up with too narrow slit.
In practice, we select the slit, translate this to angular resolution and select the camera focal length to match the pixel scale.
Notes: <number>

## Slide 10: Putting some numbers
<number>
Home work
The spectrograph for the BWT is based on a 20 cm grating with a blaze angle of 66.5º and 72 grooves per mm
  Find angular resolution of the grating at 4000 Å, 6000 Å and 8000 Å
  Find optimal slit size with collimator length of 80cm
  Take a realistic seeing (2”) and the corresponding entrance slit size. Compute the resolution R and the camera focal length to achieve 3 pixel sampling of a resolution element (15 micron pixel size)
  Why is it hard to make high-resolution spectrometers for large telescopes? How the size of the primary mirror affects parameters and dimensions of a spectrometer?
Notes: <number>

## Slide 11: Modern concept
<number>
Echelle gives high resolving power (high orders) and high efficiency (no dark stripes)
Spectral orders overlap (maximum reflection at blaze angle)  order selection or cross-disperser is needed (e.g. grating or prism)
Central wavelength of order m is given by:
With a cross-disperser the whole spectrum is packed in a rectangular 2D format, perfect for an electronic detector
Notes: <number>

## Slide 12: Spectrograph designs
<number>
Echelle, white pupil (e.g. SALT-HRS)
Notes: <number>

## Slide 13: Echelle focal plane layout
<number>
Notes: <number>

## Slide 14: Side effects
<number>
Orders are curved
Order spacing changes
Short FSR
Camera aberrations directly affect resolution
Hard to calibrate fringing
Notes: <number>

## Slide 15: Other spectroscopic instruments
<number>
IFU instruments 2D image slices are re-arranged in 1D slit. E.g. SINFONI
Multi-object instruments. E.g. FORS, FLAMES
Notes: <number>

## Slide 16: Fabry-Perot interferometer
<number>
The resolution is determined in the same way as for a grating
Transmission/Reflection ratio depends on the wavelength
The ratio between the reflection and the transmission peaks is called finesse
F-P is often used as tunable filter
Finesse high low
http://www.physik.uni-osnabrueck.de/kbetzler/sos/fabryperot.pdf
Notes: <number>